This page was exported from Chemgrout [    https://www.chemgrout.com    ]

Export date: Thu Apr 18 21:41:51 2024 / +0000 GMT

# CG-460 High Pressure Colloidal Series

Product Page: https://www.chemgrout.com/products/colloidal-mixing-equipment/double-acting-plunger-grout-pumps-colloidal-mixing-equipment/cg-460-high-pressure-colloidal-series-copy/

## Product Summary

### Product Description

Download Specification

The versatile ChemGrout model CG460/2X8 is a skid mounted, high-pressure grout plant that is designed to mix and pump neat cements at high-pressures. The CG460 features two high shear colloidal 55-gallon (208 liter) mixing tanks, and a double acting, high-pressure plunger type grout pump. Dual 55 gallon colloidal mix tanks allow for independent mixing of flushing and structural grouts.  Each mixer is equipped with variable speed, high-efficiency, high shear disks, rotating at speeds up to 3,000 rpm that provides rapid and thorough mixing. The tank outlet valves are a large 4” butterfly type that assures full material flow into pump suction. The grout pump is a double acting, positive displacement plunger style that will deliver 15 GPM (57 l/m), 2000 PSI (138 BAR).

### Applications

Hollow Bars, Grouted Anchors, Tiebacks, Post Grouting, Shaft Sealing, Water Cutoffs and Hydro Electric Dam Grouting.

### Specifications

| Pump Size | Maximum Output | Maximum Pressure |
| --- | --- | --- |
| 2" x 8" | 15 GPM (57 LPM) | 2,000 PSI (138 BAR) |

### Requirements, Weights, and Dimensions

| Model Number | Description | Dimensions | Weight |
| --- | --- | --- | --- |
| CG460/2X8/A | Skid Mounted Air Powered HP, High Shear Colloidal Grout Plant Requires 375 CFM (10.6 M3/Min.) @ 100 PSI (7 bar) air | 96"L x 40"W x 56"H | 1,400lbs |
| CG460/2X8/H | Skid Mounted Hydraulic Powered HP, High Shear Colloidal Grout Plant Requires 3 Circuits, 2@6gpm, 2400 psi-mixers, 1@16gpm, 2400 psi-pump | 108"L x 40"W x 56"H | 1,320 lbs |
| CGPU25/EH | Skid Mounted Electric/Hydraulic Power Pack Requires 25 HP-3 phase power, several voltage options available | 85"L x 36"W x 46"H | 1,240lbs |
| CGPU49/DH4 | Skid Mounted Diesel/Hydraulic Grout Plant Self-contained, Utilizes Kubota 49 HP Tier 4 Diesel Engine | 85"L X 36"W X 46"H | 1,450lbs |

## Product Gallery

Product added date: 2016-07-21 13:17:27

Product modified date: 2021-08-09 14:27:42

Product export as MS Document by WooCommerce PDF & Print plugin.