This page was exported from Chemgrout [    https://www.chemgrout.com    ]

Export date: Thu Apr 18 14:47:09 2024 / +0000 GMT

# CG-3CL8 Progressive Cavity Grout Pumps

Product Page: https://www.chemgrout.com/products/grout-pumps/progressing-cavity-pumps-flanged-inlet/cg-l8-progressive-cavity-grout-pumps/

## Product Summary

### Product Description

The ChemGrout model CG3CL8 are skid mounted grout pumps.  These units feature a 70-gallon holding hopper and a size 8, flanged inlet, progressing cavity grout pump.  Larger hoppers and suction hoses are available upon request.  The holding hopper is connected directly to the suction of the pump for a continuous pumping operation.  The grout pump is a 3 stage, size 8, variable speed, positive displacement, progressive cavity, rotor-stator pump that will deliver 22-44 GPM, 261 PSI..  All components are easily accessible for operating, cleaning and maintenance.

### Applications

Soil & rock, void filling, waterproofing, anchor, cable, rock bolts, encasements, well casing, abandon shafts/holes, spraying topcoats, underlayments, slabjacking, slab raising, cable stays, post tensioning, slurry cutoff walls, anchors, roadway repair, dowel rod grouting, floor restoration, slab undersealing, mudjacking, soil stabilization, pressure grouting, window & door frame grouting, building construction, self-leveling underlayment, and floor topping.

### Specifications

| Model Number | Description | Dimensions | Weight |
| --- | --- | --- | --- |
| CG3CL8/H | Hydraulic Grout Plant Requires 13 gpm, 2400 psi | 110" L X 41" W X 43" H | 1100 lbs. |
| CG3CL8/EHT | Elec./Hyd. Grout Plant Requires 25 amps, 3 Phase | 110" L X 41" W X 43" H | 1675 lbs. |
| CG3CL8/GHES | Gas/Hyd. Grout Plant 24 HP Engine, Electric Start | 110" L X 41" W X 43" H | 1,630 lbs. |
| CG3CL8/DH | 24 HP Diesel/Hyd. Grout Plant | 110" L X 43" W X 43" H | 1,730 lbs. |

## Product Gallery

Product added date: 2016-01-06 14:12:47

Product modified date: 2023-08-14 10:37:03

Product export as MS Document by WooCommerce PDF & Print plugin.